## Slide 1
MoPA-PD · arXiv 2111.06383 · CoRL 2021 · Alternative approaches · Dec 9
Stakeholder 1 / 13
DEC 9 · ALTERNATIVE APPROACHES · STAKEHOLDER
Buy the pattern, not the checkpoint.
MoPA-PD turns a privileged motion planner into a visual policy you can ship without it. Liu*, Uppal*, Sukhatme, Lim, Englert, Lee — CoRL 2021.
Push 100 / 32.0 / 110.8
Assembly 0 → 100
DR ≥ 96.7 sim-to-sim
Sim has geometry. Deploy is vision. Clutter is the hard part. That is the buy. The 2021 Sawyer 32×32 checkpoint is not.
Notes: Stakeholder open.
• Paper: Distilling Motion Planner Augmented Policies into Visual Control Policies. MoPA-PD. arXiv 2111.06383. CoRL 2021. Code: clvrai.com/mopa-pd.
• Authors, equal first: I-Chun Arthur Liu* and Shagun Uppal*; Sukhatme, Lim, Englert, Lee. USC CLVR + RESL.
• Seat: Dec 9, Alternative approaches. All seats empty — equal depth. Not a foundation-model prehistory talk.
• One-liner: lock the privileged-MP → vision-student alternative before pure VLA weeks. Buy the pattern, not the 2021 Sawyer checkpoint.
• Chips are Table 1 and Table 2, not estimates. Fig. 2 is Push, Lift, Assembly in MuJoCo — not a household robot.

## Slide 2
MoPA-PD · arXiv 2111.06383 · CoRL 2021 · Alternative approaches · Dec 9
Stakeholder 2 / 13
SHARED SPINE · TATTOO ON EVERY DECK
Five facts that do not change with the seat
01
Train privilege
Classical MP (RRT-Connect) lives inside MoPA-RL (Yamada et al., CoRL 2020). Geometry and the planner are train-time infrastructure, not the shipped controller.
02
Distill, then smooth
Visual BC on direct-action rollouts removes the planner and smooths RRT jitter. MoPA-PD then runs asymmetric SAC: actor from BC, critic from MoPA-RL Q, Re:Rπ = 1:3, small α.
03
Deploy is planner-free pixels
Inference is a 32×32 image plus joints. No RRT-Connect, no object state, no motion planner. The critic’s state privilege ends when training ends.
04
Numbers you must be able to say
Push 100 / 32.0 / 110.8 (ASR / AEL / ADR). Assembly 0 without BC-smooth vs 100 with. DR ≥ 96.7 sim-to-sim (Lift Scenario 1 is worst). Expert Push AEL 111 vs Ours 32.
05
What this paper is not
Not an ancestor of ACT, Diffusion Policy, π₀, OpenVLA, or OXE — contrast poles only. Not a JEPA / LeWM / Cosmos child. Sim-only Sawyer. Do not launder DR into sim-to-real.
Notes: Shared spine — say this before the role-specific argument.
• Privileged classical MP (RRT-Connect) at train inside MoPA-RL (Yamada 2020) → visual BC (smooths jitter, drops the planner) → MoPA-PD asymmetric SAC → planner-free pixels at deploy.
• Must-cites: Push 100 / 32.0 / 110.8 (ASR/AEL/ADR). Assembly 0 without BC smoothing vs 100 with. DR ≥ 96.7 sim-to-sim; Lift Scenario 1 is the worst cell. Expert Push AEL 111 vs Ours 32.
• NOT an ancestor of ACT, Diffusion Policy, or VLAs (π₀ / OpenVLA / OXE). CLEAR contrast poles only. NOT a JEPA / LeWM / Cosmos child.
• Sim-only Sawyer MuJoCo, 32×32 images. Real robot is future work in the conclusion. Refuse to launder domain randomization into sim-to-real.
• Preserve paper numbers only. Do not invent BEHAVIOR success rates or a real-robot SR.
• Stakeholder use: these five lines are the buying brief. The rest is when to buy, when to walk, and which risks you will not paper over.

## Slide 3
MoPA-PD · arXiv 2111.06383 · CoRL 2021 · Alternative approaches · Dec 9
Stakeholder 3 / 13
WHY THIS SEAT EXISTS
Classical robotics is still a training superpower
Obstructed exploration
Sparse contact around boxes and furniture is where pure visual SAC dies. Table 1: Asym. SAC and MoPA-Asym. SAC are 0. A planner that can see geometry is how the demos exist.
Productization, not the product
MoPA-RL already solves the tasks in state space. MoPA-PD’s job is to throw the planner and the mesh away at deploy, and to shorten the path while doing it.
Not a TAMP stack
A distillation recipe for obstructed visuomotor control. Not a hierarchical planner library and not a BEHAVIOR skill API. Teach the pattern; do not assign the repo as the platform.
The alternative to demo-only
When teleop and OXE-scale data are thin and sim geometry is honest, privileged exploration beats waiting for more human demos. That is the Alternative-approaches argument.
Notes: Why schedule MoPA-PD under Alternative approaches.
• Clean story for “why not only VLA-from-demo?”: in heavily obstructed sim, privileged MP exploration makes the demos. Distillation is the productization step.
• HIGH motion-planning / obstruction hook without a full TAMP stack. Do not overclaim hierarchy.
• Asym. SAC is 0/0/0 (Assembly ADR 3.4 only). MoPA-Asym. SAC is 0/0/0. Putting the planner inside a visual loop is not enough.
• MoPA-RL state expert ASR is already 98.2 / 95.0 / 99.8. The extra claim is a visual policy with better path length.

## Slide 4
MoPA-PD · arXiv 2111.06383 · CoRL 2021 · Alternative approaches · Dec 9
Stakeholder 4 / 13
FIG. 1 · THE FACTORY
Spend privilege in sim. Ship pixels.
Stage 0
MoPA-RL SAC. Small Δq is direct. Large Δq calls RRT-Connect. Full state.
Stage 1
Visual BC, MSE, 32×32. Drops the planner. Smoothed rollouts become the expert buffer Re.
Stage 2
Asymmetric SAC. Actor from pixels. Critic from state. Init, low α, 1:3 mix.
Notes: Walk Fig. 1 left to right. Do not skip Stage 0.
• Stage 0: enlarged action Ã. Direct band is small joint deltas. Larger deltas invoke RRT-Connect (Kuffner & LaValle) for collision-free paths. State SAC.
• Stage 1: rollouts stored in direct action space. Visual BC by MSE. Side effect the paper insists on: BC smooths jitter, because the planner optimizes avoidance, not smoothness.
• BC still has covariate shift (Ross et al.). Stage 2 is required.
• Stage 2: deployed actor is image + joints. Critic sees full state only in sim. Init: actor ← BC, critic ← MoPA-RL Q, legal because MoPA-RL’s action space supersets direct actions.
• SAC samples Re and the agent buffer at 1:3. α starts lower than MoPA-RL’s final α so the visual agent exploits the prior.
• Re is BC trajectories, not raw planner data. Jitter in the replay is why Assembly dies.

## Slide 5
MoPA-PD · arXiv 2111.06383 · CoRL 2021 · Alternative approaches · Dec 9
Stakeholder 5 / 13
BUY / WALK
Buy when geometry, vision deploy, and clutter line up
BUY THE PATTERN
Sim collision geometry is real
An RRT, TAMP, or MoPA-style teacher can run offline. If the mesh is a lie, Stage 0 dies.
Deploy must be vision
No planner latency and no object-state sensor on the robot. That is the product constraint.
Clutter is the bottleneck
Reach into a box, lift out, insert among obstacles. Pure visual RL does not explore this.
WALK TO ANOTHER POLE
Abundant teleop or OXE-scale data
Prefer ACT, Diffusion Policy, or a VLA. MoPA-PD is a sim recipe, not a replacement head.
No reliable collision model
Nothing privileged to distill. Do not invent a planner to justify the pipeline.
Cross-embodiment generality
One Sawyer in MuJoCo. Use the idea. Do not ship the checkpoint.
Notes: Buy / walk. The left column is the only honest purchase.
• Buy: accurate sim geometry, vision-only deploy, clutter as the hard part. Pattern = MP or TAMP teacher → BC smooth → vision RL or IL.
• Walk: abundant teleop or OXE-scale language tasks → ACT / Diffusion Policy / VLA. Complementary, not a successor, not an ancestor.
• Walk: no collision geometry. Stage 0 cannot run.
• No cited chain into π₀ or OpenVLA. Do not brief one.

## Slide 6
MoPA-PD · arXiv 2111.06383 · CoRL 2021 · Alternative approaches · Dec 9
Stakeholder 6 / 13
TABLE 1 · THE EFFICIENCY BUY
Same success. Much shorter paths than the expert.
PUSH AEL
111 → 32.0
Expert MoPA-RL vs MoPA-PD. Push ADR moves 52.7 → 110.8. The policy is not cloning the planner. It is shorter.
ASR is the wrong headline on Push and Assembly: BC-Visual is already 99.4 and 97.0. The buy is AEL / ADR, plus Lift (BC 62 → 99).
Notes: Do not sell raw success on Push.
• Ours: Push 100.0/32.0/110.8. Lift 99.0/42.0/101.7. Assembly 100.0/61.7/84.5.
• MoPA-RL Push 98.2/111.0/52.7. About 3.5× longer. ADR 52.7 vs 110.8.
• BC-Visual: 99.4/118.0/46.9 · 62.0/108.8/34.6 · 97.0/115.1/50.4.
• Horizon 250 is why failures show AEL 250. Eval: 5 seeds × 100 episodes after 3M steps (teacher 1M + distill 2M). γ=0.99. Success < 0.05. Bonus +150.
• You are buying a shorter visual policy, not a higher scoreboard on an already-solved push.

## Slide 7
MoPA-PD · arXiv 2111.06383 · CoRL 2021 · Alternative approaches · Dec 9
Stakeholder 7 / 13
RISKS YOU WILL OWN IF YOU BUY IT
Four costs the abstract does not waive
Sim-only. Tax unpaid.
The conclusion names real-world fine-tune and a vision critic as future work. Table 2 is sim-to-sim. Do not brief this as a robot result.
32×32, one arm
Sawyer 7-DoF, MuJoCo, three tasks, tiny RGB. Not wrist cameras, not multi-embodiment, not a household camera stack.
Stage 0 is engineering
You need a working MoPA-RL or another MP teacher, plus collision checks. Frozen demos are the practical path. The planner is not free.
The critic is still privileged
Asymmetric actor-critic (Pinto et al.) sees full state while learning. “Vision-only” is an inference claim, not a training claim.
Notes: Read all four risks. Do not soften the first.
• §5: fine-tuning in the real world with a vision critic, or sim-to-real techniques, is “definite future work.”
• DR randomizes texture, color, lighting. Test scenes add distractors, walls, furniture, table size. Still MuJoCo. Still Sawyer.
• Visual actor: 3-layer CNN, 3× FC-256, LeakyReLU, 32×32. Transfer the recipe, not the representation.
• Do not propose “just run SAC on the robot.” The critic story does not survive that sentence.
• Pitch: clutter-exploration prior. Not a competitor to π₀-scale generalists.

## Slide 8
MoPA-PD · arXiv 2111.06383 · CoRL 2021 · Alternative approaches · Dec 9
Stakeholder 8 / 13
FIG. 4 + TABLE 2
Robust in sim. Not a sim-to-real receipt.
DO NOT LAUNDER
Worst cell is Lift, Scenario 1: ASR 96.7. The paper’s claim is >96% on three unseen sim scenarios. Appearance shift is not a real robot.
Notes: The picture is the whole argument: textures and distractors inside MuJoCo.
• Table 2 ASR Push/Lift/Assembly. Original 99.7/99.3/100.0. Scenario 1: 100.0/96.7/100.0. Scenario 2: 99.3/97.3/100.0.
• Push Scenario 2 ADR is printed 99.04. Quote that precision if you read the cell.
• No non-DR control column. Do not invent a “without DR” delta.
• Sentence: we bought appearance robustness in simulation. We did not buy sim-to-real.

## Slide 9
MoPA-PD · arXiv 2111.06383 · CoRL 2021 · Alternative approaches · Dec 9
Stakeholder 9 / 13
CONTRAST POLES · NOT A FAMILY TREE
Where modern stacks win, say so
ACT / ALOHA
Chunked CVAE cloning from human teleop. Different data, different action interface. Use it when demonstrations are what you actually have.
Diffusion Policy
Generative action chunks from demos. Not a privileged-planner distill. Table 1 does not beat it — that baseline did not exist here.
π₀ / OpenVLA / OXE
Large multi-task vision-language-action. MoPA-PD is single-task sim distillation. No cited ancestry. Do not brief one.
DART, separately
DART labels recoveries by disturbing the expert. MoPA-PD amortizes a planner. Shared covariate-shift vocabulary. Not the same product.
Notes: Contrast only. Do not invent descent.
• ACT and Diffusion Policy: human/teleop demos. MoPA-PD demos come from a privileged MP-RL teacher.
• π₀, OpenVLA, Open X-Embodiment: no cited chain. “Ancestor” is a false claim.
• LeWM / JEPA / Cosmos are world-model poles. Mention only to refuse the filing. Do not build the talk on them.
• RoboGen keeps MP primitives in the loop. MoPA-PD’s deploy story is the opposite: the planner leaves. Parallel, not a child.
• Ross, Gordon, Bagnell 2011 is the shared covariate-shift citation with the DAgger family. Methods differ.

## Slide 10
MoPA-PD · arXiv 2111.06383 · CoRL 2021 · Alternative approaches · Dec 9
Stakeholder 10 / 13
WHAT THE PURCHASE ORDER SAYS
Pattern in. Checkpoint out.
In
An MP or TAMP teacher when sim geometry is trustworthy. BC smoothing before any RL buffer. A vision actor at deploy. Path length, not just success.
Out
2021 32×32 weights. Online RRT on the robot. A claim that DR solved reality. Any sentence that starts “this is why VLAs work.”
Budget shape
Paper protocol: 3M steps × 5 seeds × 3 tasks, after a 1M-step teacher. The only printed times are BC (Table 8): 30 / 39 / 120 min. Full RL GPU time is unstated.
Decision
Fund the pattern on the next cluttered sim task that already has a mesh. Do not fund a Sawyer reproduction as a product milestone.
Notes: Close the buy.
• Product line: a sim distillation factory. Spend privileged MP + state to mint visual policies that no longer carry planner latency or state sensors.
• Table 8: Push 12 epochs / 30 min; Lift 13 / 39; Assembly 24 / 120. Selection is first epoch at 100% validation success, not lowest test MSE (Fig. 9).
• Do not quote a GPU-hour number for the full paper. It is not in the PDF.
• “Does this replace our VLA?” No. “Can a planner in sim teach a vision policy for clutter?” Inside MuJoCo, this paper’s yes.

## Slide 11
MoPA-PD · arXiv 2111.06383 · CoRL 2021 · Alternative approaches · Dec 9
Stakeholder 11 / 13
FIG. 2 · THE ONLY PRODUCT SURFACE
Three obstructed Sawyer tasks. Nothing else was scored.
Push
Reach into a box. Push the red cube onto the green goal. ASR is easy for BC. Path length is not.
Lift
Reach, grasp, lift a can out without collisions. BC-Visual ASR falls to 62. Stage 2 earns its place.
Assembly
Insert the fourth table leg among the other three. IKEA furniture env. Dies without BC smoothing.
Notes: Fig. 2, Yamada et al. tasks, re-used. MuJoCo, Sawyer 7-DoF, 32×32, horizon 250.
• Do not generalize the picture into a kitchen. It is a box, a can, and a table.
• Assembly is Lee, Hu, Lim, ICRA 2021 furniture assembly — one insert, not a BEHAVIOR activity.
• Stakeholder use: name which task matches the buyer’s clutter. If none do, you are selling an analogy, and you should say so.

## Slide 12
MoPA-PD · arXiv 2111.06383 · CoRL 2021 · Alternative approaches · Dec 9
Stakeholder 12 / 13
LANGUAGE FOR THE BRIEFING
Sentences that survive contact with the PDF
Say
“Train-time RRT-Connect inside MoPA-RL, distilled to a visual policy.”
Say
“Push episodes went from 111 steps to 32, at full success.”
Say
“Domain randomization held up in unseen sim scenes, worst cell 96.7.”
Don’t say
“We have a sim-to-real manipulation system.”
Don’t say
“This is an early VLA / ACT / diffusion policy.”
Don’t say
“It works on BEHAVIOR.” Nothing in the paper ran that benchmark.
Notes: Briefing language. Read the don’t column last so it sticks.
• The three say-lines are Table 1 and Table 2, scoped.
• If a stakeholder asks for a robot video, the honest answer is: the authors list real fine-tuning as future work. The project page is clvrai.com/mopa-pd; do not promise it contains a real-robot result you have not watched.

## Slide 13
MoPA-PD · arXiv 2111.06383 · CoRL 2021 · Alternative approaches · Dec 9
Stakeholder 13 / 13
STAKEHOLDER CLOSE
Say this, then stop
ONE-LINER
Lock the privileged-planner → vision-student alternative before the pure VLA weeks. Buy the pattern. Do not buy the 2021 Sawyer checkpoint.
Remember
Push 100 / 32.0 / 110.8. Assembly dies at 0 without BC smoothing.
Refuse
Sim-to-sim DR is not sim-to-real. No invented robot success rate.
Notes: Stop on the one-liner. Do not add a roadmap.
• Follow-up experiments belong to the Empiricist seat: a smoke is not Table 1.
• “Is this how π₀ was trained?” No.
• Project page, from the abstract: https://clvrai.com/mopa-pd